## Slide 1: Arduino
Freek Pols

## Slide 2: The Arduino
Pin in or out
usb
Power
supply
Analog in
Voltage and 0 V
microcontroller

## Slide 3: The breadboard
Colom connected
Row connected

## Slide 4: The coding environment
compiling
upload
Serial monitor
Com-poort

## Slide 5: Tinkercad coding environment

## Slide 6: LED and resistors
A LED draws 20 mA (2,0V).
The applied voltage is 5,0 V.
So…

## Slide 7: Assignment 1
Build the circuit.
Set the resistor to 220 Ω
Start the simulation (no code required)
Explain what is happening.

## Slide 8: Assignment 2
Build the circuit.
See that the 5V is not used!
Copy + paste the Blink code in the code environment
Start the simulation.
Change the code so the LED blinks faster.

## Slide 9: Assignment 3
Expand the existing circuit to the one you see here.
Write your code so all three LEDs can be controlled.
Make a trafficlight.

## Slide 10: Code
Arduino code consist of three / four parts
Define variables before the setup
Setup which runs a single time
An infinite loop
Functions
Code explained
int rodeled = 13;
void setup() {
// initialize digital pin 13 as an output.
pinMode(rodeled, OUTPUT);
}
void loop() {
digitalWrite(rodeled, HIGH);
delay(1000);
digitalWrite(rodeled, LOW);
delay(1000);
}

## Slide 11: PWM ~
Pin 3, 5, 6, 9, 10 & 11 are PWM pins
PWM stands for Pulse Width Modulation
The output voltage is controlled by PWM

## Slide 12: Assignment 4
Copy the Fade code.
Connect the LED to pin 9.
Change your code so the cycle is shorter.
Why do we use analogWrite()?

## Slide 13: Code
int is an integer and refers to pin (11) or to a variable which is used.
This variable can be used throughout your code.
In the setup we define whether our variable is an out/input pin.
Explaining the code.
int led = 11;
int brightness = 0;
int fadeAmount = 5;
void setup() {
pinMode(led, OUTPUT);
}
void loop() {
analogWrite(led, brightness);
brightness = brightness + fadeAmount;
if (brightness == 0 || brightness == 255) {
fadeAmount = -fadeAmount ;
}
delay(30);
}

## Slide 14: Assignment 5
Build the circuit.
Copy & paste the script Button.
Explain the code and what is happening when you push the button.